## Slide 1: GIS Workshop Pt 1
Summer Data Science Series

## Slide 2: Goals:
Projections & coordinate systems
Loading spatial data
Building new layers
Editing data (and metadata)
Making and exporting basic maps
Exporting data

## Slide 3: Projections
Mercator
Lambert Conformal
Azimuthal Equidistant

## Slide 4: Projections
Area-preserving – Equal Area
Shape-preserving – Conformal or orthomorphic
Distance-preserving – Equidistant, displays the accurate distance between one point and all other points
Direction-preserving – Includes conformal, orthomorphic, and azimuthal projections (only from the central point)

## Slide 5: Coordinate Systems
How to place where you are on earth and how you report those coordinates
  DMS: 40 degrees, 42 minutes, 51 seconds
  Decimal Degrees: 40.714
Web Mercator is default projection for Web Mapping
WGS1984 is common coordinate system (EPSG:4326)

## Slide 6: Loading spatial data
Add Data
  Points, Lines, Polygons, & CSV
Create Points from Table
  CSV
Make NetCDF Raster Layer
  NetCDF

## Slide 7: Building New Layers
For Building Shapefiles (Points, Lines, Polygons)
  Catalog View> folders > [right click on project ] > new > Shapefile
  Edit Tab > Create > select layer you want to build
  Make sure you save your edits
For Rasters
  Create Raster Dataset

## Slide 8: Editing Layers
For Editing (Points, Lines, Polygons)
  Edit Tab > Modify > select tool > select layer
  Make sure you save your edits
Other useful tool:
  Clip (analysis tool)
  Clip Raster (Data Management Tool)
    Note: If something clips weird from a netCDF. Export it to a .tiff first then re-upload and clip

## Slide 9: Change Coordinate System or Projection
To see all coordinate systems being used
  [Right click on Map in drawing order panel] > properties > coordinate system
To change dataset coordinate system
  Define Projection (data management tool)

## Slide 10: Mapping!
Insert tab > new layout (choose size)
Map frame (choose extent)
Toggle layers on and off on left panel
Can change symbology and re-name layers from left panel
  Right click layer and choose symbology or properties>general to name
Add scale bar and north arrow and legend from top row
  Right click on legend and click properties to change unit

## Slide 11: Exporting data and maps
Map
  Share > export layout (will open panel on the right) > export
    DON’T FORGET TO HIT EXPORT
Data
  Right click > data > export features